## Slide 1: Design Space Exploration of Deep Neural Networks
CSCE 790
By Yang ren, rui xin, Hassan Alamri

## Slide 2: Overview
Introduction
Hardware Platform
Models and Datasets
Experiment approach
Some insights
Sampling strategy
Parameters Interaction
Measurement Prediction
Interesting observation
Conclusion

## Slide 3: Introduction
Many real-world applications have limitations in hardware resources
  Autonomous cars
  Mobile devices
We want to explore hardware & compiler-level configurations on DNN models, given constrained hardware resources
How changing in configuration space affects DNNs’ in terms of:
  Inference time
  Power consumption

## Slide 4: Hardware Platform
Nvidia Jetson TX1
Parallel computation
Widely used in deep neural networks applications
Specs:
  Maxwell GPU Architecture with 256 CUDA cores
  64-bit quad-core ARM A57 CPUs
  4GB LPDDR4
  16 GB eMMC
  Voltage: 5.5 V-19.6 V DC
  Maximum module power: 6.5 W-15 W

## Slide 5: Models and Datasets
Models
  Resnet50 on Keras
  VGG16 on Keras -> we observed more memory errors
Datasets
  Cifar10 image dataset

## Slide 6: Cont. : Models and Datasets
Reference: https://openreview.net/pdf?id=Bygq-H9eg

## Slide 7: Experiment approach
Experiment using sampling as a client & server as a host for DNNs

## Slide 8: Cont. : Experiment approach
Some Important procedures in running experiment:
  Maximize hardware resources for other tasks:
    For instance: loading datasets
  Power consumption is captured every 0.5 seconds, then take average:

## Slide 9: Cont. : Experiment approach
Dimension space for our experiments
Hardware Configuration
  CPU frequency ~ range between ( 102 MHz , 1.73 GHz )
  Number of disabled cores ~ range (0 , 3)
  GPU frequency ~ range between (76 MHz , 998 MHz)
  EMC frequency ~ range between (80 MHz , 1.6 GHz)
Compiler-level Configuration
  Batch Size ~ in range (1, 4, 16, 32)
  Allow Growth ~ in range (0 , 1)
  Memory fraction per GPU ~ in range (0.15, 0.2, 0.25, 0.3, 0.33)

## Slide 10: Some insights
CPU Freq | # disabled cores | GPU freq | EMC freq | Batch Size | Allow Growth | Memory Frac per GPU | Inference Time | Module Power Cons | GPU Power Cons | CPU Power Cons
612 MHz | 2 | 460.8 MHz | 1.33 GHz | 16 | 1 | 0.33 | 24.1s | 4976 | 1391.3 | 368.2
1.326 GHz | 2 | 998.4 MHz | 1.06 GHz | 1 | 0 | 0.15 | 25.5s | 7541.6 | 3688.9 | 630.5
1.224 GHz | 1 | 384 MHz | 1.06 GHz | 32 | 0 | 0.3 | 20.8s | 5623.6 | 1758.2 | 676.5
306 MHz | 3 | 307.2 MHz | 1.6 GHz | 16 | 0 | 0.25 | 38.7s | 4226.2 | 873.2 | 214
1.555 GHz | 3 | 768 MHz | 1.33 GHz | 16 | 0 | 0.25 | 14.5s | 7171.3 | 2828.2 | 893.0
102 MHz | 3 | 307.2 MHz | 1.06 GHz | 32 | 1 | 0.15 | 104.2s | 2872.8 | 339.7 | 82.6
163.2 MHz | 2 | 614.4 MHz | 800 MHz | 1 | 1 | 0.2 | 29.7s | 7376.0 | 3433.3 | 823.8
204 MHz | 0 | 844.8 MHz | 1.6 GHz | 1 | 0 | 0.15 | 54.6s | 4790.6 | 1434.3 | 227.8

## Slide 11: Cont. Some insights
Experiment failures
CPU Freq | # disabled cores | GPU freq | EMC freq | Batch Size | Allow Growth | Memory Frac per GPU | Inference Time | Module Power Cons | GPU Power Cons | CPU Power Cons
1.734 GHz | 2 | 998.4 MHz | 4.8 MHz | 32 | 1 | 0.2 | NA | NA | NA | NA
816 MHz | 2 | 460.8 MHz | 4.8 MHz | 32 | 1 | 0.2 | NA | NA | NA | NA
102 MHz | 3 | 76.8 MHz | 4.8 MHz | 32 | 1 | 0.2 | NA | NA | NA | NA
102 MHz | 3 | 76.8 MHz | 4.8 MHz | 1 | 1 | 0.2 | 707.9 | 2598 | 268.2 | 168.7
1.734 GHz | 0 | 998.4 MHz | 1.6 GHz | 32 | 0 | 0.1 |  | NA | NA | NA
1.734 GHz | 0 | 998.4 MHz | 1.6 GHz | 8 | 0 | 0.1 | 10.9 | 9671.7 | 5028.9 | 1098.6
1.734 GHz | 0 | 998.4 MHz | 1.6 GHz | 64 | 1 | 0.1 | NA | NA | NA | NA
Low memory frequency
It works with lowest batch size
Batch size 64 result in failure
Memory fraction works with low batch size

## Slide 12: Sampling Strategy
Discretize continuous parameters:
For example:
  CPU Frequency = 917 MHz -> Closest(917 MHz)  918 MHZ
  GPU Frequency = 840 MHz -> Closest(840 MHz)  844.8 MHz
  Batch size = 18.222 -> Closest (18.222)  16
  Memory Fraction = 0.2788 -> Closest (2.78888)  0.3

## Slide 13: Cont. : Sampling Strategy
We want to explore configuration space
but, It takes time and effort…. and it costs a lot
For our experiments, for instance:
  7 dimensional space, and each has different number of values
  Total number of experiments = CPU freq × disabled cores × CPU freq × EMC freq × batch size × growth × memory frac per GPU
  Total number of experiments = 18 × 4 × 15 × 4 × 4 × 2 × 6 ≈ 207k
  Clearly, that is not practical at all, given the dimension space!

## Slide 14: Cont. : Sampling Strategy
We need to tune hyperparameters to minimize both:
  Inference time
  Power consumption
But, we also want to explore the trade-off…..
Again, to evaluate the objective functions:
  A lot of computation and interaction with outside system
  Time ~ 5 minutes average
Clearly, the objective functions are expensive to evaluate!

## Slide 15: Cont. : Sampling Strategy
We opted to go with Bayesian Optimization (BO), because of:
Black-box optimization
Small number of function evaluations
Exploit regions that yield good points
And explore regions with high uncertainty
With small number of evaluations, it builds an informative model
Based on Gaussian Process (GP)
  Uses previously observed parameters to make an assumption about unobserved parameters.
Acquisition Function used to intelligently suggest the next set of parameters

## Slide 16: Cont. : Sampling Strategy
Initial Sampling
  Latin-Hyper Cube  selection of parameters by even sampling method
Optimization function
  Multi-Objectives Bayesian Optimization  Inference and Power Consumption
Hypervolume-based probability of improvement
  Focus on density and uniformity of Pareto set
  One cost function for multi-objective functions to balance between them

## Slide 17: Cont. : Sampling Strategy Resnet50
Using resnet50 model
Bayesian multi-objective approach using GPflowOpt python library
Pareto frontier is the allocation of pareto set efficiency
Potentially optimal points
It enables us to make trade-off
Pareto Frontier

## Slide 18: Cont. : Sampling Strategy Resnet50
On Resnet50 model

## Slide 19: Cont. : Sampling Strategy Resnet50
Bayesian Optimization
We can clearly see the drops in both inference and power consumption
Bayesian optimization starts minimizing the values after 10th evaluated points.

## Slide 20: Cont. : Sampling Strategy Resnet50
Comparison between Bayesian optimization and Random Search for evaluated points.
Inference time in Bayesian optimization seems to be dropped earlier than Random Search.

## Slide 21: Cont. : Sampling Strategy Resnet50
Comparison between Bayesian optimization and Random Search for evaluated points.
Power consumption in Bayesian optimization drops significantly

## Slide 22: Cont. : Sampling Strategy VGG16
On VGG16 model

## Slide 23: Cont. : Sampling Strategy VGG16
Comparison between Bayesian optimization and Random Search for evaluated points.
Inference time in Bayesian optimization seems to be not dropping.

## Slide 24: Cont. : Sampling Strategy VGG16
Comparison between Bayesian optimization and Random Search for evaluated points.
Power consumption in random search drops significantly

## Slide 25: Parameters Interaction Resnet50
Polynomial function for Inference Time with Degree 3 is the best to describe the data and interaction.
Degree 3 is more accurate with lowest RMSE value.

## Slide 26: Cont. : Parameters Interaction Resnet50
The same goes for power consumption.
Degree 3 is more accurate with lowest RMSE value.

## Slide 27: Cont. : Parameters Interaction Resnet50
Polynomial functions for inference and power consumption

## Slide 28: Cont. : Parameters Interaction
We empirically observed that data obtained from Bayesian Optimization on Resnet50 have roughly lowest RMSE, and more accurate for predication.
Meanwhile, data obtained from Random search on VGG16 have roughly lowest RMSE, and more accurate for predication.
But, we are still curious and need another evidence……
Gradient Boosting Regression
  Ensembling technique
  Uses a set of predictors to yields better results
  Controls the variance of a model to build a complex predictive function

## Slide 29: Cont. : Measurement Prediction Resnet50
Random
Bayesian Optimization
RMSE: 3.08
RMSE: 20.16

## Slide 30: Cont. : Measurement Prediction Resnet50
Random
Bayesian Optimization
RMSE: 826.34
RMSE: 897.15

## Slide 31: Cont. : Measurement Prediction VDD16
Random
Bayesian Optimization
RMSE: 4.2
RMSE: 4.5

## Slide 32: Cont. : Measurement Prediction VDD16
Random
Bayesian Optimization
RMSE: 2470.6
RMSE: 2052.4

## Slide 33: Interesting observation
Image classification by Resnet50
Label | Probability
hartebeest | 0.8069511
sunscreen | 0.27676105
chain_saw | 0.6491425
Japanese_spaniel | 0.22487636
Label | Probability
hartebeest | 0.80695164
sunscreen | 0.27676108
chain_saw | 0.64914304
Japanese_spaniel | 0.22487622
Label | Probability
hartebeest | 0.80695087
sunscreen | 0.27676052
chain_saw | 0.6491422
Japanese_spaniel | 0.22487634
Configuration 1
Configuration 2
Configuration 3
Slight changes in probability

## Slide 34: Conclusion
Resnet50 & VGG16 with 100 images from Cifar10 dataset used for experiments
We show the advantage of using Bayesian Optimization to tune hyperparameters in both Resnet50 & VGG16
Surprisingly, Random search seems to be better in VGG16
We show the interaction of parameters using polynomial functions.
We also present another model for prediction
If we have time:
  Handle missing values in Bayesian Optimization
  Experiments with different models and datasets
  Explore the accuracy of image classification given the configuration space

## Slide 35
THANK YOU 